## Slide 1
MCU
MMIO & Interrupt
On-chip Peripheral
(eg, GPIO, SPI, UART, ETH, SD)
Off-chip Peripheral
(eg, sensors, radio, screen)
Pin
MCU Structure
MCU
Peripheral MMIO
Vendor HAL, Platform HAL
RTOS,
Protocol Stack,
Off-chip Peripheral Lib
App
Programming Model
Introduction (MCU)
HAL (Hardware Abstract Layer)

## Slide 2
MCU
Vendor HAL, Platform HAL
RTOS
Protocol Stack
Off-chip Peripheral Lib
App
Standard
Introduction (Programming)
MCU
App
Bare metal
Peripheral MMIO
Peripheral MMIO
MCU
App
Hybrid
RTOS,
Protocol Stack
Off-chip Peripheral Lib
Lib
Vendor HAL
Platform HAL
Peripheral MMIO
High development efficiency
Fine-grained control
Less power, Faster speed
Balance
Standard Firmware
Non-Standard Firmware
Non-Standard Firmware

## Slide 3
Introduction (Emulator)
MCU
App
Peripheral MMIO
App
Qiling
Unicorn
How did I develop Qiling before?
Reversing peripheral interface logic and translate them into Python code.
What needs to do for reversing peripheral interface logic？
Read the official doc day by day.
Develop the firmware of target peripheral.
Observe the register access sequence.
Understand the official HAL Lib logic.
Shortage
stm32 is famous for its rich doc, but not all company’s peripherals have detailed doc.
Not all peripherals require high-precision simulation, firmware just do simple check.’
The logic of different peripherals has a lot in common, catch them !!

## Slide 4
Auto/Semi-auto Reversing
- HAL Library represents the peripheral interface, finding a way to pass these functions but not need to read a lot of doc.
- Find the same pattern cross different peripheral.
Is symbolic execution the best method?
Do it on source code or binary?

## Slide 5
Auto/Semi-auto Reversing
Input: Standard Firmware (need source code)
Output: Peripheral Logic (Python code in Qiling) / New Qiling.
Training the Qiling through auto-reversing the standard firmware, and the new engine can emulate all firmware.
Workflow:
Find all HAL function (entry/exit point) through elf.
Do symbolic execution when enter entry point.
Trying to match the preset pattern, find the most simple pattern to pass the code.
After exiting the HAL function, add new logic into qiling.
Restart from 1, but ignore the reversed HAL function,

## Slide 6
Related work
HALucinator: Firmware Re-hosting Through Abstraction Layer Emulation
  Requires the firmware use a HAL, and the HAL must be available to the analyst (e.g., either open source, or part of the microcontroller’s SDK)
  The effectiveness of LibMatch, especially when the compiler or library versions used is unknown, is limited.
  Just run the firmware, do not know the peripheral interface logic.

## Slide 7
Related work
- P2IM: Scalable and Hardware-independent Firmware Testing via Automatic Peripheral Interface Modeling
Did not consider the mutual influence of registers, and the register model is not flexible enough.
Registers are identified and categorized by monitoring access to the memory-mapped peripheral region.
The model generalizes peripheral registers into four types and provides the access patterns and handling strategy for each type.

## Slide 8
Related work
- Jetset: Targeted Firmware Rehosting for Embedded Systems
Key Insight: It is designed to ignore most paths through the firmware to focus on a particular target piece of code.
Approach: Jetset use heuristic search and symbolic execution to find the path to target code.
Difference: Neither P2IM nor Jetset really care peripheral logic, they just want to skip the code related to peripheral access, and then fuzzing at the target point. It is hard to find the peripheral-related bug. (Concurrency bug)

## Slide 9
Experiment
  STM32F407, STM32F411, STM32F103
  SAM3X8E
  GD32VF103 – RISCV, Rust (more arch)
  BES2300 (real world example)
  MK64FN1M0VLL12 (optimal)
Platform
  Ethernet (TCP, UDP, HTTP)
  Filesystem (SD card, Fatfs)
  Drone (Emuflight, betaflight)
  RTOS (FreeRTOS, RT-thread)
  PLC (optimal)
Software
  GPIO
  UART, SPI, I2C
  TIM, RTC
  SDIO, SD Card
  ETH
  CRC, RNG
  ADC, DAC
Peripheral
  Completeness
  Correct rate
  Pattern coverage / number
  Fuzzing result (optimal)
Parameter